TITLE 35: ENVIRONMENTAL PROTECTION

SUBTITLE B: AIR POLLUTION

CHAPTER I: POLLUTION CONTROL BOARD

SUBCHAPTER K:  EMISSION STANDARDS AND LIMITATIONS FOR MOBILE SOURCES

PART 240

MOBILE SOURCES

SUBPART A:  DEFINITIONS AND GENERAL PROVISIONS

Section

| 240.101 | Preamble |
| --- | --- |
| 240.102 | Definitions |
| 240.103 | Prohibitions |
| 240.104 | Inspection |
| 240.105 | Penalties |
| 240.106 | Determination of Violation |
| 240.107 | Incorporations by Reference |

SUBPART B:  EMISSIONS

Section

| 240.121 | Smoke Emissions |
| --- | --- |
| 240.122 | Diesel Engine Emissions Standards for Locomotives |
| 240.123 | Liquid Petroleum Gas Fuel Systems |
| 240.124 | Vehicle Exhaust Emission Standards (repealed) |
| 240.125 | Compliance Determination (repealed) |

SUBPART C:  SMOKE OPACITY STANDARDS AND TEST PROCEDURES FOR DIESEL-POWERED HEAVY DUTY VEHICLES

Section

| 240.140 | Applicability |
| --- | --- |
| 240.141 | Smoke Opacity Standards and Test Procedures for Diesel-Powered Heavy Duty Vehicles |

SUBPART D:  STEADY-STATE IDLE MODE TEST EMISSION STANDARDS

Section

| 240.151 | Applicability |
| --- | --- |
| 240.152 | Steady-State Idle Mode Vehicle Exhaust Emission Standards |

| 240.153 | Compliance Determination |
| --- | --- |

SUBPART E:  TRANSIENT LOADED MODE TEST EMISSION STANDARDS

Section

| 240.161 | Applicability |
| --- | --- |
| 240.162 | Vehicle Exhaust Emission Start-Up Standards |
| 240.163 | Vehicle Exhaust Emission Final Standards |

240.164

240.165

Vehicle Exhaust Emission Fast-Pass Standards

Compliance Determination

SUBPART F:  EVAPORATIVE TEST STANDARDS

Section

| 240.171 | Applicability |
| --- | --- |
| 240.172 | Evaporative System Integrity Test Standards |
| 240.173 | Evaporative System Purge Test Standards (Repealed) |

SUBPART G:  ON-ROAD REMOTE SENSING TEST EMISSION STANDARDS

Section

240.181	Applicability

240.182	On-Road Remote Sensing Emission Standards

Compliance Determination

SUBPART H:  ON-BOARD DIAGNOSTIC TEST STANDARDS

Section

240.191	Applicability

240.192	On-Board Diagnostic Test Standards

240.193	Compliance Determination

| 240.Appendix A | Rule into Section Table |
| --- | --- |
| 240.Appendix B | Section into Rule Table |

| 240.Table A | Vehicle Exhaust Emission Start-Up Standards |
| --- | --- |
| 240.Table B | Vehicle Exhaust Emission Final Standards |

240.Table C	Vehicle Exhaust Emission Fast-Pass Standards

AUTHORITY:  Implementing Sections 9, 10 and 13 and authorized by Sections 27 and 28.5 of the Environmental Protection Act [415 ILCS 5/9, 10, 13, 27, and 28.5] and Section 13B-20 of the Vehicle Emissions Inspection Law of 1995 [625 ILCS 5/13B-20]; implementing Section 13-109.2 of the Illinois Vehicle Code [625 ILCS 5/13-109.2].

SOURCE: Adopted as Chapter 2: Air Pollution, Part VII: Mobile Sources, filed and effective April 14, 1972; codified at 7 Ill.  Reg.  13628; amended in R85-25, at 10 Ill.  Reg.  11277, effective June 16, 1986; amended in R90-20 at 16 Ill.  Reg.  6184, effective April 7, 1992; amended in R94-20 at 18 Ill.  Reg.  18013, effective December 12, 1994; amended in R94-19 at 18 Ill.  Reg.  18228, effective December 20, 1994; amended in R98-24 at 22 Ill.  Reg.  13723, effective July 13, 1998; expedited correction at 22 Ill. Reg. 21120, effective July 13, 1998; amended in R01-12 at 24 Ill. Reg. 19188, effective December 18, 2000; amended in R01-8 at 25 Ill. Reg. 3680, effective February 26, 2001; amended in R02-8 at 25 Ill. Reg. _____, effective __________.

BOARD NOTE:  This part implements the Environmental Protection Act as of July 1, 1994.

NOTE:  Capitalization denotes statutory language.

SUBPART H: ON-BOARD DIAGNOSTIC TEST STANDARDS

Section 240.191	Applicability

The standards of this Subpart apply to all 1996 and newer model year light duty vehicles, light duty trucks 1, and light duty trucks 2 that are required to meet the standards contained in 40 CFR § 86.094-17 and which are inspected utilizing the on-board diagnostic test procedures contained in 35 Ill. Adm. Code 276.209. Vehicles that receive a result of fail do not thereby fail their emissions test until January 1, 2002. However, this date shall be extended to January 1, 2003, if the Agency petitions the USEPA for such an extension, and the request for an extension is approved by the USEPA pursuant to 40 CFR § 51.357(a)(12).

(Source:  Amended at 25 Ill. Reg.           , effective                       p)

Section 240.192	On-Board Diagnostic Test Standards

Vehicles subject to on-board diagnostic testing shall fail the on-board diagnostic test if one of the following occurs:

the vehicle connector is missing, has been tampered with, or is otherwise inoperable; or

the malfunction indicator light is commanded to be illuminated and it is not visually illuminated according to visual inspection; or

the malfunction indicator light is commanded to be illuminated for and any of the following on-board diagnostic trouble codes are present (where x refers to any digit):; or

Any PX1XX Fuel and Air Metering codes

Any PX2XX Fuel and Air Metering codes

Any PX3XX Ignition System or Misfire codes

Any PX4XX Auxiliary Emission Controls codes

P0500 Vehicle Speed Sensor Malfunction

P0501 Vehicle Speed Sensor Range/Malfunction

P0502 Vehicle Speed Sensor Circuit Low Input

P0503 Vehicle Speed Sensor Intermittent/Erratic/High

P0505 Idle Control System Malfunction

P0506 Idle Control System RPM Lower Than Expected

P0507 Idle Control System RPM Higher Than Expected

P0510 Closed Throttle Position Switch Malfunction

P0550 Power Steering Pressure Sensor Circuit Malfunction

P0551 Power Steering Pressure Sensor Circuit Malfunction

P0552 Power Steering Pressure Sensor Circuit Low Input

P0553 Power Steering Pressure Sensor Circuit Intermittent

P0554 Power Steering Pressure Sensor Circuit Intermittent

P0560 System Voltage Malfunction

P0561 System Voltage Unstable

P0562 System Voltage Low

P0563 System Voltage High

Any PX6XX Computer and Output Circuits Codes

P0703 Brake Switch Input

P0705 Transmission Range Sensor Circuit Malfunction (PRNDL Input)

P0706 Transmission Range Sensor Circuit Range/Performance

P0707 Transmission Range Sensor Circuit Low Input

P0708 Transmission Range Sensor Circuit High Input

P0709 Transmission Range Sensor Circuit Intermittent

P0719 Torque Converter/Brake Switch “B” Circuit Low

P0720 Output Speed Sensor Circuit Malfunction

P0721 Output Speed Sensor Circuit Range/Performance

P0722 Output Speed Sensor Circuit No Signal

P0723 Output Speed Sensor Circuit Intermittent

P0724 Torque Converter/Brake Switch “B” Circuit High

P0725 Engine Speed Input Circuit Malfunction

P0726 Engine Speed Input Circuit Range/Performance

P0727 Engine Speed Input Circuit No Signal

P0728 Engine Speed Input Circuit Intermittent

P0740 Torque Converter Clutch System Malfunction

P0741 Torque Converter System Performance or Stuck Off

P0742 Torque Converter System Stuck On

P0743 Torque Converter System Electrical

P0744 Torque Converter System Intermittent

d)	the malfunction indicator light (MIL) does not illuminate at all when the vehicle is in the key-on/engine-off condition.

(Source:  Amended at 25 Ill. Reg.           , effective           p)

Section 240.193	Compliance Determination

Compliance shall be determined based upon the inspection of the on-board diagnostic vehicle connector, malfunction indicator light, and electronic retrieval of data stored in the vehicle’s  on-board diagnostic system fault codes using the on-board diagnostic test procedures that will be adopted by the Agency in 35 Ill. Adm. Code 276.

(Source:  Amended at 25 Ill. Reg.           , effective                      p)